## Slide 1: Introduction to Optoelectronic Devices

## Slide 2: Outline
What is optoelectronics?
Major optoelectronic devices
Current trend on optoelectronic devices

## Slide 3: What Did the Word “Opto- Electronics” Mean?
Optoelectronics is the study and application of electronic devices that interact with light
Electronics (electrons)
Optics (light or photons)
Optoelectronics

## Slide 4: Examples of Optoelectronic Devices

## Slide 5: Major Optoelectronic Devices — Direct Conversion Between Electrons and Photons
Light-emitting diodes (LEDs) (display, lighting,···)
Laser diodes (LDs)
(data storage, telecommunication, ···)
Photodiodes (PDs) (telecommunication, ··· )
Solar Cells (energy conversion)

## Slide 6: Light-Emitting Diodes (LEDs)
6
Light-emitting diode (LED) is a semiconductor diode that emits incoherent narrow-spectrum light when electrically biased in the forward direction of the p-n junction.

## Slide 7: Photon Emission in Semiconductor
E
F
E
C
EV
Valence band
Conduction band
Photon
Eg
When an electron meets a hole, it falls into a lower energy level, and releases energy in the form of a photon.
The wavelength of the light depends on the band gap of the semiconductor material
Semiconductor materials: Si, Ge, GaAs, InGaAs, AlGaAs, InP, SiGe, etc

## Slide 8: Semiconductor Materials vs. LED Color
General Brightness |  |  |  | 
GaP | GaN | GaAs | GaAIAs | --
Green, Red | Blue | Red, Infrared | Red, Infrared | --
Super Brightness |  |  |  | 
GaAIAs | GaAsP | GaN | InGaN | GaP
Red | Red, Yellow | Blue | Green | Green
Ultra Brightness |  |  |  | 
GaAIAs | InGaAIP | GaN | InGaN | --
Red | Red, Yellow, Orange | Blue | Green | --

## Slide 9: Application of LEDs
Display
Solid-state lighting
Communication
Remote control, etc
LED lights on an Audi S6

## Slide 10: Laser Diodes (LDs)
Lasers (Light Amplification by Stimulated Emission)
Photon emission processes:
Absorption Photodetectors
Spontaneous emission LEDs
Stimulated emission Lasers

## Slide 11: Photo Diodes (PDs)
A photodiode is a semiconductor diode that functions as a photodetector. It is a p-n junction or p-i-n structure. When a photon of sufficient energy strikes the diode, it excites an electron thereby creating a mobile electron and a positively charged electron hole

## Slide 12: PDs’ Detection Range and Materials
Material
Silicon (Si) Germanium (Ge)
Indium gallium arsenide
(InGaAs)
Lead sulfide (PbS)
Wavelength range (nm)
190–1100
400–1700
800–2600
<1000-3500

## Slide 13: Vision of Solar Cells (Photovoltaics)
Solar Energy
•
•
•
Free
Essentially Unlimited Not Localized
Solar Cells
•
•
•
•
•
•
Direct Conversion of Sunlight  Electricity No Pollution
No Release of Greenhouse-effect Gases No Waste or Heat Disposal Problems
No Noise Pollution — very few or no moving parts
No transmission losses — on-Site Installation
Why solar cells?

## Slide 14: Residential and Commercial Applications
14
Challenges:
cost reduction via: a) economy of scales b) building integration and
c) high efficiency cells

## Slide 15: Trends in optoelectronic devices
15
Long wavelength, high power light sources or photodetectors
Nanoscale devices
Low cost, easy fabricated materials
High opto-electronic conversion efficiency
Multi-wavelength sources

## Slide 17: Advantages of Optical Comm.